Pebble HD with Black and White or Coloured Buttons

HC107 and HC108

Please retain these instructions for future reference. These instructions are also available in other formats.

Special Warning: This special order product is non-returnable unless faulty.

Contents

General description	2

Items supplied with the	2

Orientation	2

Front	2

Back	3

Top edge	3

Bottom edge	3

Using the product	3

Connecting the AC adaptor/power supply	3

Charging the battery	4

Using the Rechargeable Battery	4

Turning the Power On/Off	5

Button Combinations	5

Entering the Menu	5

Adjusting the Image Size	5

Viewing Modes	6

Freezing an Image (Snapshot function)	6

Saving a Snapshot	7

Recalling a Saved Snapshot	7

Deleting a Saved Snapshot/All Snapshots	7

Turning LED Lighting ON/OFF	8

Using the Clock & Time/Date Feature	8

Using the Carrying Case	8

Adjusting the Handle	9

Reading Position (fully closed)	9

Hand-Held Position (180˚ open)	9

Writing Position (210˚ open)	9

Hands-Free/Desktop Position	9

Using the Menu	9

User Settings	9

Product Settings	10

Factory Settings	10

Image Gallery	10

Setting the Clock Time/Date	11

Connecting to your PC	11

Transferring Images to your PC	11

Firmware Update	11

Product Information	12

Master Reset	12

TROUBLESHOOTING	12

SAFETY PRECAUTIONS	13

Technical specification	14

Warning	15

How to contact RNIB	15

Terms and conditions of sale	15

# General description

The Pebble HD is a handheld electronic video magnifier that you can take anywhere. Weighing less than 8 ounces, Pebble HD features a uniquely-designed folding handle and includes both near-viewing and table reading modes. Small enough to fit in your pocket or purse, the Pebble HD is the ideal companion to provide magnification, on the go.

HC107 - Pebble HD with Black and White buttons

HC108 - Pebble HD with Coloured buttons

## Items supplied with the

Pebble HD

Lens Cloth

Carrying Case with belt clip

AC adaptor power supply

USB to Mini Power Cable (used for Domestic power supply and Firmware Upgrade)

## Orientation

### Front

The front of the Pebble HD has a recessed rectangular screen. On the right of the screen are two buttons, one with a plus symbol and the other with a minus symbol. The top button increases the magnification (button with plus symbol), while the bottom reduces the magnification (button with minus symbol).

To the left of the screen, in the middle is a button with a circle symbol. This changes the viewing mode – this is the mode button.

On the left bottom edge are two LED status indicators.

### Back

The handle is predominately white but with a black grip either side and is T-shaped with a gap in the centre. It is attached underneath the magnification buttons. Fold out for hand-held viewing or close for reading at a table.

With the handle folded out and on the right there is a speaker grill towards the top and on the left. In the centre there is a raised circular lens for the camera and either side of this are recessed LEDs.

### Top edge

On the top edge, in the centre is the USB power socket. This socket is orientated with the larger side closest to the back of the Pebble HD. To the right of the socket, towards the handle is a round red button, this is the freeze frame button.

### Bottom edge

On the bottom edge is a central green button which is the power On/Off button. To the right of this, closer to the handle is a red, square button which is the Gallery button.

# Using the product

Your Pebble HD can be powered using:

The included AC adaptor/power supply

Integrated rechargeable battery (included)

Your Pebble HD is packaged with the integrated battery partially charged. We highly recommend that you plug your Pebble HD into a power socket in order to fully charge the integrated battery prior to using the device for the first time.

Note: When the Pebble HD is on and an AC Adapter, or USB cable (connected to a PC), is connected to the Pebble HD an ‘Hour Glass’ symbol will appear.  During this time (approximately 15-20 seconds) the Pebble HD will determine which type of connection has been made.

When the AC Adapter is connected - the Pebble HD will go into ‘Live’ mode.

When a USB Cable is connected (also connected to a PC) - a USB Symbol will appear.

## Connecting the AC adaptor/power supply

Use the following procedure to connect the Pebble HD to the AC adaptor/power supply.

Connect the tip of the included AC Adaptor/power supply to the Mini-USB connector port.

Plug in the remaining end of the AC Adaptor/power supply to an available AC wall outlet or USB port on your PC.

## Charging the battery

### Using the Rechargeable Battery

Your Pebble HD includes a rechargeable battery that can be continuously charged inside the Pebble HD, even while the unit is in operation. It is recommended to leave the unit connected with the included AC adaptor when the unit is not in use to maintain a continuous charge on the battery. This way, your Pebble HD will always be ready for portable use.

It is not possible to overcharge the included battery.

Important Points When Using Battery Power:

- The rechargeable battery should be fully charged prior to the first use.

- When fully charged your Pebble HD should last up to 2.5 to 3.0 hours battery life depending on the LCD Brightness setting.

#### Battery Charging Procedure

To charge the Lithium Ion battery inside your Pebble HD, simply connect the included AC adaptor/power supply. You can continue to use the Pebble HD even while the battery is being charged.

#### Charging the Pebble HD when not in use (Standby)

To charge the Pebble HD when it is not in use:

Press the Green [POWER] button to enter ‘Standby’ mode after connecting the AC Adaptor/power supply (or USB Cable to a PC). To return to normal operation ‘Press and release’ the Green [POWER] button again.

#### Built-In Battery Charger Status Indicators

Your Pebble HD has two small indicator lights (LEDs) located on the side of the unit. The LEDs indicate the current power state and charge status of the batteries.

Refer to the section below for more information regarding the meaning of each LED indicator light:

Blue LED on, Amber LED off when using mains power - AC plugged & Battery Charging

Blue LED on, Amber LED On when using mains power - AC plugged & Battery is full

Blue LED off, Amber LED on when using battery power - Battery good/full

Blue LED off, Amber LED on and flashing when using battery power - Battery low

Blue LED on and flashing, Amber LED off when using battery power – Standby

Blue LED off, Amber LED off when using battery power – Unit is off

Note: When your Pebble HD battery is getting low, approximately 15 minutes before shutoff, a ‘chime’ will sound, with a battery icon displayed for 2 seconds.

#### Battery Charge Indicator

Once the Pebble HD powers on, and when it comes out of ‘Standby’ mode, a Battery Charge Status indicator will appear for 2 seconds (during this time all button functions are disabled).

(Pebble HD with low charge will power off after 3-5 seconds if not connected to adaptor)

## Turning the Power On/Off

Use the following procedure to turn the power of your Pebble HD On or Off:

Find the recessed Green [POWER] button.

To turn the Pebble HD on, press and hold the Green [POWER] button for 1 second or more until the screen lights up. You will hear a ‘start-up’ sound and an image will appear on the LCD display.

To turn off the Pebble HD, press and hold the [POWER] button again for 2 seconds or more. A short, confirmation tone will be heard when the unit is powered Off.

Note: To put the Pebble HD into ‘Standby’ mode, once powered on, ‘Press and release’ the [POWER] button. To return to ‘live’ mode ‘Press and release’ the

[POWER] button again. Disconnecting the Adapter, or USB connection, from the Pebble HD when it is in ‘Standby’ mode will cause the Pebble HD to power off.

## Button Combinations

Throughout this User Manual there will be ‘button combinations’ (i.e. Press the [MODE] and Red [FREEZE] buttons). This indicates that the buttons should be pressed simultaneously.

## Entering the Menu

The Pebble HD has configurable options that can be modified by using the System Menu.  You may enter System Menu by pressing [MODE] + [FREEZE]. To navigate press [Zoom plus or minus] and the Yellow Highlight will move to your selection.

The Red [FREEZE] Button is used for confirming selections or advancing deeper into the menus.

The [MODE] Button is used for cancelling selections or returning to previous menus.

## Adjusting the Image Size

Use the following procedure to adjust the magnification (size) of the image on the LCD.

ZOOM buttons:

Press the [+] ZOOM button to increase the magnification size on the LCD.

Press the [-] ZOOM button to decrease the magnification size on the LCD.

There are 5 ‘fixed’ zoom levels on the Pebble HD. Pressing and Holding the [+] or [-] ZOOM button for more than 1 second activates a ‘continuous zoom’ mode.

## Viewing Modes

Use the following procedure to select the viewing mode of the image on the LCD display:

By pressing the [MODE] button you can cycle through the 7(if enabled) pre-set viewing modes. To change your colour selects to any of the 28 available, enter the System Menu (see “Entering Menu” above). Then while on the first highlight Enter User Settings >> Display >> Preferred Modes, which will have all of your available options. Use the [Freeze] button to confirm.

Note: Hold [MODE] for 2 seconds to return back to ‘Full Colour’ mode. The ‘Colour  Mode  Selection’  menu  allows  all  of  the Viewing  modes,  except  ‘Full  Colour’  (factory  default), to be temporarily disabled (See colour modes below).

There are two configurable colour pre-sets referred to as Deluxe and Basic Factory Settings.

Deluxe Colour Modes:

Full Colour Image (Factory Default – always ON)

Positive Image (Factory = White background / Black text)

Negative Image (Factory = Black background / White text)

Colour Select 1 (Factory = Green On Black)

Colour Select 2 (Factory = Yellow On Black)

Colour Select 3 (Factory = Yellow On Blue)

Black and White Image

Basic Colour Modes:

Full Colour Image (Factory Default – always ON)

Black and White Image

Positive Image (Factory = White background / Black text)

Negative Image (Factory = Black background / White text)

## Freezing an Image (Snapshot function)

If desired, you can take a snapshot (Freeze) of an image on the display. You can also adjust the size and change viewing modes after freezing an image. This feature is quite useful for reading price tags, prescriptions or other information that may need to be temporarily captured.

Use the following procedure to take a snapshot (Freeze) of the image on the display:

Press the Red [FREEZE] button to capture the image. Pebble HD will make a “Camera shutter” sound when the image is captured and the LED lights will turn off. After capturing the image you can adjust the size or ‘enabled’ viewing modes as desired.

Press the Red [FREEZE] button again to exit and resume normal operation. Turning off the power of your Pebble HD will also clear the frozen image.

### Saving a Snapshot

You can also save a ‘snapshot’ image (approximately 300) on the Pebble HD to view at a later time.

After freezing the image, press and hold the [FREEZE] button for 2-3 seconds. You will see a Saving Icon displayed and the Pebble HD will then return to normal operation mode when save is complete.

### Recalling a Saved Snapshot

Once you have a saved snapshot image you can ‘recall’ it and view it from the Image Gallery. To recall a saved snapshot image:

Press and hold the Orange Button [Gallery] for 3 seconds – the last saved snapshot will be displayed (in this mode LED lights are off).

To view the next/previous saved snapshot:

Use the [ZOOM +] to move up or the [ZOOM -] to move down.

To select the image press the Red [FREEZE] button.

You can increase/decrease Zoom using [+/-]

Change Viewing Modes by pressing [MODE]

To Delete an Image press and hold the [FREEZE] button for more than 2 Seconds.

To go back to the Image Gallery press the [FREEZE] button

To resume normal operation press the [GALLERY] for 3 seconds if you entered from live screen or [MODE] button if you entered via menu.

### Deleting a Saved Snapshot/All Snapshots

You can delete images from your Gallery by either removing them one by one or deleting all images at once.  Use the instructions below for both operations.

Remove a Single Image

Enter the Gallery from the System Menu or Live Screen

Press and Hold Orange [Gallery] Button to enter into the Gallery from the Live Camera Preview

When Viewing an Image Press the [Freeze] button for more than 2 seconds to delete an individual Snapshot.

The waste bin icon will display indicating that the image has been deleted.

Remove All Images:

Navigate to the Entry Marked “Image Gallery” at the bottom of the system menu.

You will have two options on this screen:

Display Images - Pebble HD enters Gallery Mode and you view your pictures normally

Delete All Images – a confirmation message will pop up with CANCEL or CONFIRM. Selecting CONFIRM will delete all snapshots and Return you to the menu (an “All Images Deleted” message will be displayed on the LCD)

## Turning LED Lighting ON/OFF

Your Pebble HD has built-in LED lighting to illuminate your reading material.

It is also possible to turn OFF the built-in LED lighting, if desired. This may be useful when magnifying certain objects with a highly reflective surface, such as a watch or glossy photo.

Use the following procedure to turn off the LED lighting:

With the Pebble HD power turned on, Press and Hold the [Mode] button then press the [+] SIZE together.

An icon will appear on the display to indicate the LEDs have powered off.

To restore the LED lighting use the same combination as before.

Note: Each time the Pebble HD is powered on, it will automatically default to the factory setting with the LED lights ON.

## Using the Clock & Time/Date Feature

The Pebble HD can maintain, and display, the current Time & Date once it is set. To set the current Time/Date see the “Setting the Clock Time/Date” section.

To View the clock on live screen

Press the [MODE] + [ZOOM -] for more than 3 seconds

To return to live screen after checking the clock

Press the [MODE] + [ZOOM -] again for more than 3 seconds to exit.

## Using the Carrying Case

For added protection, your Pebble HD includes a convenient carrying case with a belt clip. This helps to protect your Pebble HD from accidental damage when “on-the-go”.

When not using the Pebble HD, return it to the case for added protection. The carrying case is designed to be attached securely to your belt. Please ensure that your Pebble HD is in the folded position before inserting into the carrying case.

## Adjusting the Handle

The Pebble HD features a unique adjustable handle, which can rotate, allowing you to easily magnify a wide variety of objects in various positions.

### Reading Position (fully closed)

Close the handle completely into a folded position. Adjusting the handle in this position is convenient for reading a book, pamphlet or other printed text.

### Hand-Held Position (180˚ open)

Open the handle. Adjusting the handle in this position is convenient for magnifying a wide variety of objects.

### Writing Position (210˚ open)

Open the handle as if for the hand-held position. Then, holding the handle on the work surface, lift the screen towards the handle so that it rotates upwards and stays in a position of roughly 210˚. The viewing screen now tilted upwards allows to write underneath.

### Hands-Free/Desktop Position

Open the handle at a slight angle, 180˚ or 210˚ for hands-free or desktop use. You can use it with the handle at around 70˚-80˚ so that the screen is portrait in front of you and the handle is on the work surface, or use in the 210˚ position. Adjusting the handle in this position is convenient when both hands are needed to perform other tasks.

## Using the Menu

### User Settings

User Settings is designed to allow users to set their own custom configuration and preferences. Upon exiting the User Settings submenu, all selected options are saved.

#### Languages

Select from any of the available languages.

#### Audio

Sound, Audible items including mechanical sounds

#### Display

Visuals and display items including icons and graphical User Interface indicators, Extended Zoom & Colour Modes

#### Time & Date

Clock, Time and Date

### Product Settings

This menu allows you to configure product features such as:

#### Auto Standby

Set Standby Times from 5, 10, 20, or 30 Minutes

#### Configure Buttons

Enable or disable the following buttons: Save, Freeze, Gallery, Image Panning, and Clock.

### Factory Settings

The Factory Settings submenu is designed to provide access to product and system information as well as reset the device to factory settings when needed.

NOTE: After Factory Reset the System Settings may need to be reset based on your location.

#### Product Information

This is your Pebble HD’s individual product information. This may be needed if the supplier needs to know your model etc. It will list the following titles followed by the information for your individual model after each title:

Product SN: (Your model’s info)

Software RN: (Your model’s info)

Boot RN: (Your model’s info)

Board SN: (Your model’s info)

Language Group: (Your model’s info)

#### Reset Deluxe Settings

This option allows you to reset the device to its original factory default settings. All features are available through the Deluxe Setting.

#### Reset Basic Settings

This option allows user to reset the device to its Basic or limited feature setting. In this mode the Freeze, Image Pan, Image Save, and Gallery options are all disabled.

### Image Gallery

Image Gallery is designed to provide you with a simple graphical user interface to view and select desired saved files and/or images for viewing. Saved files will be stored on the internal mini SD card. File names are time stamped to indicate the time of the capture/save. While in the Gallery a user can view their saved images or delete these images.

## Setting the Clock Time/Date

Note: While you are setting the time and date the item that is ready to be ‘set’ will be highlighted.

The Pebble HD can maintain, and display, the current Time & Date once it is set. To set the current Time/Date:

- Enter the Menu by pressing the [MODE] button and the Red [FREEZE] buttons (on the top and left side) together.

- Press the [FREEZE] button to select ‘User Settings’

- Using the [ZOOM -] scroll until ‘Time & Date’ is highlighted

- Press the [FREEZE] button to select ‘Set Clock’

- Again using the [ZOOM -] scroll until ‘Set Date & Time’ is highlighted

- Press the [FREEZE] button to select ‘Set Date & Time’

Using the [ZOOM +/-] change the highlighted value

Use the [FREEZE] button to set the current item and advance to the next item

Repeat steps 7 & 8 until all of the Time/Date values are set correctly*

Once the current Time & Date have been set you can choose to enable/disable the ‘24 Hour Clock’ format, and ‘Date Format’ options.

To enable/disable an option: Use the [ZOOM +/-] to highlight the desired option and press the [FREEZE] to select

Press the [MODE] button to return to normal operation.

## Connecting to your PC

### Transferring Images to your PC

Your Pebble HD has the option to upload all of your stored images to your PC. This allows you to store or share these images. Follow the instructions to upload your saved images to the PC.

- Plug the USB cable into the Pebble HD and the opposite end into the PC.

- The Pebble HD will register as a normal USB-storage device with the drive name: Removable Disk or Pebble.

- Double click the drive.

- With the drive open double click on the Image folder.

Drag or copy the images to your desktop or the desired location on your PC.

## Firmware Update

To keep your Pebble HD up to date visit our software support page at:

http://www.enhancedvision.com/support/software.html

## Product Information

Product Information will display the technical information of the Pebble HD and also allows you to restore the Pebble HD back to its factory settings.

Press the [MODE] and Red [FREEZE] buttons to enter the Pebble HD Menu.

Press the [ZOOM +/-] until “Factory Settings” is highlighted.

Press the Red [FREEZE] button to display the “Product Information” sub menu.

Press the Red [FREEZE] button again

While in these sub-menus you can:

View the Product Serial Number and firmware/software revisions

Restore the default settings of the Pebble HD by pressing the Red [FREEZE] to “Factory Restore” your device to Basic or Deluxe Configurations.

## Master Reset

If the Pebble HD is powered on, but is unresponsive – ‘Press and Hold’ the [Mode] button and press the ‘Orange’ button to reset the Pebble HD.  Press the Green power button to power the Pebble HD on again.

Note: Pebble HD must be disconnected from power to utilize the Master Reset.

## TROUBLESHOOTING

No power to the unit

• Can you power the unit using the included AC adaptor?

• Is the power supply properly connected to a surge protector or an AC outlet (mains)?

See the “Connecting the AC adaptor/power supply” and “Power Supply” section.

Video image on LCD is blurry or not clear

• Clean the LCD display and/or camera lens using the included cleaning cloth.

• Adjust the distance of the Pebble HD from your reading material or adjust the handle angle as needed to improve image quality (focus)

• Try selecting different viewing modes to improve image quality. See “Viewing modes” section.

Video image on LCD display is too bright/dark

• The Pebble HD is designed to be used in moderate lighting conditions, preferably indoors. Bright lighting (or direct sunlight) may produce shadows and/or reduce visibility. Try moving to a more shaded area to improve image quality.

• Adjust the distance of the Pebble HD from your reading material or adjust the angle of the handle as needed to improve image quality (focus)

• Try selecting different viewing modes to improve image quality

• Try adjusting the LCD brightness in the Display Submenu

Batteries will not charge

• Can you power the unit using the included AC adaptor?

• Is the power supply properly connected to a surge protector or AC mains?

See the “Connecting the AC adaptor/power supply” and “Power Supply” section.

Unit turns off automatically

• To conserve power, your Pebble HD will automatically go into standby mode after a user defined number of minutes of non-use. This is not a malfunction.

Pebble HD begins to make a “beeping” sound

• Approximately 15 minutes before shutoff the battery icon (Critical Battery) will be displayed for 2 seconds – at this point ‘Status Indicator #2’ will blink, indicating low battery .

If the battery is nearly empty, and ready to shutoff, the battery icon will be displayed with a partial ‘Red’ bar. At this point if the Pebble HD is not plugged in within 1-2 minutes it will turn off.

It also makes a beeping sound when you can’t scroll up and down in menus any further.

Unit becomes warm to the touch

Your Pebble HD integrates a camera, LCD and battery charging unit inside a very small package, but is designed to be completely safe and does not pose a risk of fire or damage. It is normal for the Pebble HD to become warm (sometimes, very warm) after extended periods of use. However, this is completely normal and does not indicate a malfunction.

## SAFETY PRECAUTIONS

For your safety and to obtain the most benefit and life from the Pebble HD, please read these important safety precautions carefully.

General guidelines for use:

Follow all warnings, cautions, and instructions marked on the product.

Use care when using the Pebble HD outdoors– it should NOT be exposed to extreme or rapid changes in temperature or humidity.

Do not place the Pebble HD near a radiator, heater or areas exposed to long hours of direct sunlight.

Prevent the risk of electrical shock by NOT attempting to disassemble the unit. Please refer all service to an authorized repair facility.

Do not use the Pebble HD in, near, or around water. The Pebble HD is not designed to offer protection against contact with liquids of any kind.

Do not use the Pebble HD during an electrical storm, lightning, or other severe weather.

Do not use the Pebble HD near open flames, flammable materials or liquids.

# Technical specification

Features:

Lightweight, portable design

200˚ adjustable handle

28 selectable viewing modes

7 levels of magnification for Pebble HD    (4.5x, 5.5x, 7.8x, 9.4x, 13.4x, *16.2x,* 20x) *Extended Zoom Feature

Image “Freeze” mode

Integrated battery charger

Power save mode (after 3 minutes of non-use)

Display:

Type: 4.3” diagonal TFT display, 16-bit

LCD Brightness: 500cd/m2 (at full brightness)

Viewing Angle: ~60˚

Physical Dimensions:

~ 5.5”L x 3.1”W x 1.25” H (with handle closed for Pebble HD 4.3”)

~ 10.2”L x 3.1”W x 1”H (with handle fully extended for Pebble HD 4.3”)

Weight: ~ 7.1 oz. for Pebble HD 4.3”x

Magnification ranges listed above are with the adjustable handle in the closed position. Minimum magnification may be reduced to 2x when the adjustable handle is fully extended.

Environment:

Operating Temperature: 32 ˚– 122˚F (0˚ – 50˚C)

Storage temperature:	-4˚ – 140˚F (-20˚ – 60˚C)

Battery:

1x 3.7V Li-Ion rechargeable battery, 3100mAh (included in Pebble HD)

Estimated Charge times (using rechargeable batteries):

~4 hours (standby mode), ~ 5.5 hours (live mode), ~ 9.5 hours (PC USB)

Estimated Usage Times (using rechargeable batteries): (Fully charged battery)**

~ 2.5 to 3 hour battery life (depending on LCD Brightness setting) (rechargeable battery included)

~ 500-1000 charge life cycles

Wall adapter:

UL/CE rated

Input: 100-240VAC 50/60Hz

Output: 5VDC, 2.1A max load

Unit:

Input: 5VDC, 2.1A max load

# Warning

To prevent condensation, do not use the unit for 1 hour after transporting the unit from extreme cold to room temperature.

All times listed are approximate. Actual Charging and Usage times may vary depending on the life cycle remaining on the battery, LCD brightness setting and other variable factors.

In the interest of continuous product improvement, specifications and/or minimum system requirements are subject to change without prior notice.

# How to contact RNIB

Phone number: 0303 123 9999

Textphone: 0845 758 5691

Web address: rnib.org.uk/shop

Postal address: RNIB, PO Box 173, Peterborough PE2 6WS, U.K.

Email: helpline@rnib.org.uk

RNIB Technology Team

Telephone 0207 391 2280

Email tfl@rnib.org.uk

Email for international customers exports@rnib.org.uk

## Terms and conditions of sale

This product is guaranteed from manufacturing faults for 24 months from the date of purchase.  If you have any issues with the product and you did not purchase directly from RNIB then please contact your retailer in the first instance.

This is a special order product so is only returnable if faulty. For all repairs contact RNIB first to help us deal efficiently with your product return.

You can request full terms and conditions from RNIB or view them online.

Registered Charity No. 226227

This product is CE marked and fully complies with all applicable EU legislation.

At the end of the product’s life you can return it to the supplier or manufacturer for free of charge disposal.  This is to comply with ‘The Waste Electrical and Electronic Equipment Directive’ (WEEE).

Date: March 2016

© RNIB