Compact+ HD portable video magnifier

HC111

Please retain these instructions for future reference. These instructions are also available in other formats.

Contents

General description	2

Items supplied with the Compact+ HD	2

Orientation	2

Front	2

Back	2

Right edge	2

Getting started	2

Using the Compact+ HD with or without the handle	2

Cleaning the mirror	3

Using the product	3

Buttons	3

Adjusting the magnification	4

Selecting a viewing mode	4

Using the snapshot button	4

Charging the battery	4

Charging the Compact+ HD	4

Standby and Auto Power Off	5

Battery warning	5

The Compact+ HD Menu	5

Activating the menu	5

Navigating the menu	6

Exiting the menu	6

Menu: Information	6

Menu: Images	6

Menu: Brightness	7

Menu: Power	7

Submenu Standby	8

Menu: Sound	8

Menu: Colour	8

Menu: Reset	9

Appendix A: Safety	9

Technical specification	9

How to contact RNIB	10

Terms and conditions of sale	10

# General description

This electronic video magnifier enables you to view and magnify printed text and images in high resolution HD quality in full colour or one of the high contrast modes. With its multifunctional design and integrated handle, the Compact+ HD can be used for reading, viewing images, price tags, displays and much more while at home or on the go.

## Items supplied with the Compact+ HD

The Compact+ HD video magnifier

A protective pouch

A power supply

A screen cleaning cloth

This user manual

## Orientation

Hold the unit in front of you so that the LCD display is facing towards you.

### Front

On either side of the display are a series of buttons; two on the left and three on the right.

The buttons on the left hand side of the screen, starting at the top, are:

- On/off

- Mode

The buttons on the right side of the screen are, from top to bottom:

- Snapshot

- Magnification button: zoom in

- Magnification button: zoom out

### Back

On the back of the unit you’ll find the camera lens with an LED light both sides and a small mirror below it.

### Right edge

There is a small blue handle which folds out from the right hand side of the unit.

# Getting started

## Using the Compact+ HD with or without the handle

The Compact+ HD is ideal to quickly scan and view objects or documents and has a collapsible, swing-out handgrip, giving you the feeling that you are using a regular magnifying glass. Simply rotate the handle clockwise, located on the underside, to release it and swing it out to snap in place. The collapsible handle gives you additional support and control for optimal reading comfort.

With the handle closed, you can use the Compact+ HD to quickly scan and view objects or documents. With the handle opened, place the Compact+ HD on the object or text you wish to view or read, and grip the handle to easily move the Compact+ HD over the object or document.

## Cleaning the mirror

For an optimal quality image, it is recommended to ensure that the mirror is kept clean. A dirty mirror will result in a fuzzy image. To clean the mirror, use the included cleaning cloth or another soft cleaning cloth.

Note: Do not use water or a cleaning agent to clean the mirror.

# Using the product

## Buttons

The Compact+ HD has the following buttons:

Mode: Pressing the Mode button to the left of the screen allows you to select one of the viewing modes. Pressing this button for three seconds will turn off the object lighting.

Magnification: Pressing the + or – button to the right of the screen allows you to increase or decrease the magnification. Pressing the + or – buttons simultaneously for one second will allow you to enter or exit the Compact+ HD menu.

Snapshot button: The white snapshot button located on the right side of the screen allows you to take a temporary picture of a text or image, enabling you to bring the image closer to your eyes. Images can be saved by pressing the snapshot button for 2 seconds.

On/Off Button: Pressing the orange On/Off button, located on the left side of the screen, for one second, will switch the unit on and off.

The camera and camera mirror of the Compact+ HD are located at the back of the unit. To the left and right of the camera are two object lights.

Switching the power on and off

To switch the Compact+ HD on for the first time, the unit needs to be charged. Once the unit is charged, press the orange On/Off button, located at the left side of the screen for one second. The unit will start up in the mode in which it was switched off. To switch off the Compact+ HD, press the orange button again for one second.

When switching on the Compact+ HD, it will take approximately 3 seconds before an image is displayed on the screen.

## Adjusting the magnification

To change the magnification settings of the unit, simply press the + or – buttons located on the right side of the screen. Press the + button to increase or the – button to decrease the magnification. The magnification range starts at 3 times and can be increased to 10 times.

## Selecting a viewing mode

Pressing the Mode button to the left side of the screen allows you to select one of the following viewing modes:

Photo mode: view full colour texts and photos

Negative mode: reading in high contrast white on black

Positive mode: reading in high contrast black on white

High contrast colour combination 1 yellow on blue

High contrast colour combination 2 yellow on black

Pressing the Mode button for 3 seconds will toggle the object lighting on or off. Switching modes will automatically turn the object lighting back on.

## Using the snapshot button

The snapshot button allows you to take a temporary picture of a text or an image.

Hold or place the Compact+ HD over the text or image you wish to capture

Press the snapshot button located on the top right side of the unit to take the snapshot

Bringing the Compact+ HD closer to your eyes will enable you to view the object or text closely

Press the Mode button to change the viewing mode

Use the magnification buttons located to the right side of the screen to change the magnification of the displayed image in 3 steps

While viewing the taken image, press the snapshot button for 2 seconds to save the image and return to the life video mode. A short beep and the onscreen indicator will confirm that the image has been saved. A maximum of 4 images can be stored inside the Compact+ HD memory. A new image will replace the oldest image in memory

Press the snapshot button again to unfreeze the image. It is now possible to take a new snapshot

## Charging the battery

### Charging the Compact+ HD

The Compact+ HD is delivered with a power supply and four country-specific power plugs. The power plugs are available in EU, US, UK and AU versions. Select the power plug appropriate to your country and mount this onto the power supply.

To charge the Compact+ HD, connect the power supply to the 5V DC IN jack, located at the left side of the unit. Plug the other side of the power supply into a power outlet. The orange LED indicator next to the 5V DC IN jack will glow continuously while the Compact+ HD is charging. When the unit is fully charged, the LED indicator will turn green. If the LED indicator flashes, there is a charging problem. In this case, disconnect the power supply and reconnect the power supply again.

Charging the Compact+ HD takes approximately 3.5 hours. A fully charged Compact+ HD can operate for an average time of 3 hours, depending on the power settings. Please note that, for safety reasons, only the power supply that was delivered with the Compact+ HD can be used to charge the unit’s battery.

If the Compact+ HD does not switch on, please make sure it is charged.

### Standby and Auto Power Off

The Compact+ HD will automatically go into standby mode after two minutes if no button is pressed or no image change is detected. Pressing any button will wake the unit up again. Four minutes after the Compact+ HD goes into standby mode, the unit will automatically switch off. Pressing the orange button on the left side of the unit will switch it back on again. The standby time and power off time can be changed or disabled in the Compact+ HD menu. Please refer to the next chapter on how to change these settings.

### Battery warning

When the battery charge is below 5% of its total capacity, a battery warning will be issued every minute by displaying the battery empty icon for 2 seconds and sounding a beep. When this occurs, be sure to charge your unit as soon as possible. When the battery is empty, the unit will automatically switch off.

If the Compact+ HD does not switch on, please make sure it is charged.

## The Compact+ HD Menu

Here’s a description on the symbols you’ll find in the menu and their meaning.

Circle with an ‘I’ in the centre: Shows the battery status and firmware version

A camera symbol: Allows you to view or delete the saved snapshots

A sun: Allows you to adjust the screen brightness

A battery: Allows you to configure the power settings

A speaker: Allows you to switch the sound on and off

A light bulb: Allows you to switch the light on and off

A square with a triangle in the top right corner: Allows you to change the colours of the high contrast modes

A curved arrow pointing to the right: Allows you to reset all factory settings to default

### Activating the menu

To enter the menu, press the + and – buttons simultaneously for one second.

### Navigating the menu

Use the + or – buttons to navigate between the menu items. The Mode button located to the left of the screen will activate the chosen menu item or confirm the selection. To change a selection, use the + or – buttons. To move back in the menu, press the snapshot button.

### Exiting the menu

To exit the menu, press the snapshot button.

### Menu: Information

This menu item shows the battery status and the current firmware version of the unit. In this menu, it is not possible to make any changes.

Activate the menu by pressing the + and – buttons simultaneously for one second

Use the + button to move up and the – button to move down within the menu Select the menu option Information and activate this menu by pressing the Mode button

To exit the menu, press the + and – buttons simultaneously for one second or press the snapshot button to go back to the previous menu

### Menu: Images

This menu contains 2 submenus:

View: To view saved images

Delete: To delete images

#### Submenu View

To view the taken images:

Activate the menu by pressing the + and – buttons simultaneously for one second

Use the + button to move up and the – button to move down within the menu

Select the menu option Images and activate this menu by pressing the Mode button

Select the View option by using the + and – buttons to scroll through the options. Press the Mode button to confirm your choice

Select the image you wish to view by using the + button to advance to the next image or the – button to go to the previous image. Press the Mode button to select the image

Use the + and – buttons to increase the magnification. Press the Mode button to change the colours

Use the snapshot button to return to video mode

#### Submenu Delete

To delete the taken images:

Activate the menu by pressing the + and – buttons simultaneously for one second

Use the + button to move up and the – button to move down within the menu. Select the menu option Images and activate this menu by pressing the Mode button.

Select the Delete option by using the + and – buttons to scroll through the options. Press the Mode button to confirm your choice

Select the image you wish to delete by using the + button to advance to the next image or the – button to go to the previous image. Press the Mode button to delete the image

Press the + and – buttons to exit the menu, or press the snapshot button to go back to the previous menu

### Menu: Brightness

This menu item allows you to adjust the brightness of the display.

Activate the menu by pressing the + and – buttons simultaneously for one second

Use the + button to move up and the – button to move down within the menu. Select the menu option Brightness and activate this menu by pressing the Mode button

Select the brightness level by using the + button to increase and the – button to decrease the brightness level. There are 5 brightness levels to choose from. The default brightness level is 5

Press the Mode button to confirm your choice

Press the + and – buttons to exit the menu, or press the snapshot button to go back to the previous menu

### Menu: Power

This menu item contains two submenus: Power off and Standby.

#### Submenu Power off

Sets the time before the Compact+ HD is automatically switched off. By default, the power off time is set to 4 minutes. These 4 minutes are activated after the default standby time of 2 minutes. By default, the unit is therefore automatically switched off after 6 minutes.

To adjust the Compact+ HD power off time:

Activate the menu by pressing the + and – buttons simultaneously for one second

Use the + button to move up and the – button to move down within the menu. Select the menu option Power and activate this menu by pressing the Mode button

Select the Power off option by using the + and – buttons to scroll through the options. Press the Mode button to confirm your choice

Select the time before the unit will power off by using the + button to increase and the – button to decrease the time. Press the Mode button to confirm your choice. Selecting DISABLED will disable the automatic power off function

Press the Mode button to confirm your choice

Press the + and – buttons to exit the menu, or press the snapshot button to go back to the previous menu

### Submenu Standby

Sets the time before the Compact+ HD goes into standby mode to conserve power. Pressing any button will take the unit out of standby mode. By default, the standby time is set to 2 minutes.

To adjust the standby time of the Compact+ HD:

Activate the menu by pressing the + and – buttons simultaneously for one second

Use the + button to move up and the – button to move down within the menu. Select the menu option Power and activate this menu by pressing the Mode button

Select the Standby option by using the + and – buttons to scroll through the options. Press the Mode button to confirm your choice

Select the time before the unit enters standby by using the + button to increase and the – button to decrease the time. Press the Mode button to confirm your choice. Selecting DISABLED will disable the automatic standby function

Press the Mode button to confirm your choice

Press the + and – buttons to exit the menu, or press the snapshot button to go back to the previous menu

### Menu: Sound

This menu item allows you to enable or disable the sounds (feedback tones). By default, the tones are enabled.

Activate the menu by pressing the + and – buttons simultaneously for one second

Use the + button to move up and the – button to move down within the menu. Select the menu option Sound and activate this menu by pressing the Mode button

To enable the sounds, select the value ON by using the + and – buttons. Press the Mode button to confirm your choice. Selecting OFF will disable the sounds

Press the Mode button to confirm your choice

Press the + and – buttons to exit the menu, or press the snapshot button to go back to the previous menu

### Menu: Colour

The Compact+ HD supports four high contrast modes. For each of these four modes, the foreground and background colours can be selected. Three of the high contrast modes can be disabled if just one high contrast mode is required.

Activate the menu by pressing the + and – buttons simultaneously

Use the + button to move up and the – button to move down within the menu. Select the menu option Colour and activate this menu by pressing the Mode button

Select the high contrast mode with the + button to move up and the – button to move down in the submenu Colour. Press the Mode button to confirm your choice

To select a new high contrast colour for the foreground and background, use the + button to move up and the – button to move down in the list of colour combinations. Select a colour combination by pressing the Mode button

High contrast modes 2, 3 and 4 can be disabled by selecting the DISABLED value

Press the Mode button to confirm your choice

Press the + and – buttons to exit the menu, or press the snapshot button to go back to the previous menu

### Menu: Reset

The Compact+ HD can be reset to the factory default settings. Any settings that have been adjusted will be restored to the factory defaults.

Activate the menu by pressing the + and – buttons simultaneously for one second

Use the + button to move up and the – button to move down within the menu. Select the menu option Reset and activate this menu by pressing the Mode button

To restore the factory defaults, select YES by using the + and – buttons. Choosing NO will leave all settings as they were

Press the Mode button to confirm your choice

Press the + and – buttons to exit the menu, or press the snapshot button to go back to the previous menu

## Appendix A: Safety

Do not expose the Compact+ HD to excessive heat or direct sunlight to avoid the risk of fire.

Do not remove any parts of the Compact+ HD. If the product is faulty, please contact RNIB helpline.

To avoid risk of electrical damage, keep your Compact+ HD away from fluids and chemicals.

Handle the Compact+ HD with care. Rough handling will damage the internal components.

Do not use the Compact+ HD near inadequately shielded medical devices.

Do not try to open the battery compartment or try to remove the battery.

Contact your dealer to service this equipment if necessary. Do not disassemble your unit as it will void the warranty.

Always unplug the system before cleaning. Use a soft damp cloth to clean the exterior. Do not use cleaning agents or abrasive materials as they will damage your unit.

Use of the Compact+ HD other than described in this manual will exclude it from warranty conditions.

# Technical specification

Magnification: 3 – 10 times

Viewing modes: Full colour photo mode; High contrast white on black; High contrast black on white; High contrast colour combination 1; High contrast colour combination 2

High contrast ratio: 500:1

High brightness screen	 average: 550 cd/m2

Screen: 4.3” TFT

Screen resolution: 480 x 272

Dimensions: 130 x 80 x 33 mm / 5.1 x 3.1 x 1.3 inches

Battery: average 3 hours continuous use; average 3 hours charging time

Li-ion battery: rechargeable, 3.7V 1400mAh

Weight: 252 grams / 8.9 ounces

Power supply type: 5 V / 1.5A

Power supply input: 100-240V, 50-60Hz, 0.3A

Power supply output:DC5V-1.5A

Net frequency: 50-60 Hz

Operating conditions

Temperature: +10°C to 35°C / 50°F to 95°F

Humidity: < 70%, no condensation

Altitudes: up to 3000 m (9842 feet)

Pressure: 700 – 1060 hPa

Storage & transportation conditions

Temperature: +0°C to 40°C / 32°F to 104°F

Humidity: < 95%, no condensation

# How to contact RNIB

Phone number: 0303 123 9999

Textphone: 0845 758 5691

Web address: rnib.org.uk/shop

Postal address: RNIB, PO Box 173, Peterborough PE2 6WS, U.K.

Email: helpline@rnib.org.uk

RNIB Technology Team

Telephone 0207 391 2280

Email tfl@rnib.org.uk

## Terms and conditions of sale

This product is guaranteed from manufacturing faults for 24 months from the date of purchase. If you have any issues with the product and you did not purchase directly from RNIB then please contact your retailer in the first instance.

For all returns and repairs contact RNIB first to get a returns authorisation number to help us deal efficiently with your product return. You can request full terms and conditions from RNIB or view them online.

Registered Charity No. 226227

This product is CE marked and fully complies with all applicable EU legislation.

At the end of the product’s life you can return it to the supplier or manufacturer for free of charge disposal.  This is to comply with ‘The Waste Electrical and Electronic Equipment Directive’ (WEEE).

Date: December 2016

© RNIB