Traveller HD Portable video magnifier

HC112

Please retain these instructions for future reference. These instructions are also available in other formats.

Contents

General description	1

Items supplied with the Traveller HD	2

Orientation	2

Front	2

Back	2

Left edge	2

Right edge	2

Getting started	2

Using the Traveller HD	3

Using the product	3

Operation	3

Slide and Read	3

Buttons	3

The Traveller HD Menu	5

Activating the menu	5

Navigating the menu	5

Exiting the menu	5

Menu options	5

Charging the battery	9

Charging the Traveller HD	9

Standby and Auto Power Off	9

Battery warning	10

Appendix A: Safety and Regulatory Notices	10

Contacting Product Support	11

Technical specification	11

How to contact RNIB	11

Terms and conditions of sale	11

# General description

The Traveller HD enables you to read, view photos, do work and so much more. The Traveller HD magnifies and enhances text, objects and images, and allows you to view them in your preferred high contrast colour combination, brightness and contrast settings. It is easy to operate and can be used at home, work and school.

## Items supplied with the Traveller HD

The Traveller HD

A protective carrying case

A power supply

A screen cleaning cloth

This user manual

## Orientation

Hold the unit in front of you so that the LCD display is facing towards you.

### Front

On either side of the display are three buttons. If you’re holding the unit in the right position, the buttons on the left side of the screen are, from top to bottom:

- Menu

- Mode

- Reading line

The buttons on the right side of the screen are, from top to bottom:

- On/off

- Zoom wheel

- Snapshot

At the bottom of the screen is a long silver area, this is the slider.

### Back

On the back of the Traveller HD is the writing stand.

### Left edge

Towards the bottom of the unit, on the left edge, is a blue circular button; this is release.

### Right edge

Towards the bottom of the unit, on the right edge, is a second blue circular button; this is also release.

# Getting started

The Traveller HD is placed correctly in front of you when the screen is facing up, and the Zoom wheel is located at the right side of the screen.

## Using the Traveller HD

The Traveller HD can only be used in the open position. The screen will be set at an ergonomic angle for an optimal reading position, while the camera will point downward. The open position enables you to read long texts and easily slide over documents.

To open the unit, follow these steps:

Place the Traveller HD in front of you so that the screen is facing up, and the Zoom wheel is at the right side of the screen.

Press the two blue Release buttons located at the outer sides of the roller. The Traveller HD screen will unlock, move up and power on.

Lift the screen until the screen locks in the up position.

To close the unit, follow these steps:

Place the Traveller HD in front of you so that the screen is facing up and in centre position, and the Zoom wheel is at the right side of the screen.

Press the two blue Release buttons located at the outer sides of the roller.

Lower the screen until the screen locks into the closed position.

Important: Only use the blue Release buttons to unlock or collapse the screen. Do not force the screen up or down.

# Using the product

## Operation

### Slide and Read

Place the Traveller HD on the document you want to read. To navigate vertically, use the roller and move the unit up and down over the document. To read or to navigate horizontally, slide the screen and move it from left to right, and from right to left to move back to the beginning of the line.

### Buttons

#### Power On / Off

To power on the Traveller HD, press the orange on / off button located above the Zoom wheel on the right side of the unit for 2 seconds. The Traveller HD will play the start-up beeps and start up in the same viewing mode as when it was powered off. Press the button for 2 seconds again to power off the Traveller HD. Depending on the power settings in the Traveller HD menu, the Traveller HD can power on when opening the unit, and power off automatically when closing the Traveller HD.

#### Adjusting the magnification

To adjust the magnification, use the Zoom wheel at the right side of the Traveller HD. Scroll up to zoom in and scroll down to zoom out.

#### Choosing viewing modes

Pressing the large blue Mode button between the Menu and Reading Line button to the left of the screen allows you to select one of the 5 viewing modes, depending on how the system is configured:

Full colour photo mode: This mode displays the original colours of the pictures and text

Reading mode 1: This mode enhances the foreground / background contrast. Pictures and text will be displayed in the configured high contrast foreground and background colour, by default black text on a white background. The foreground and background colours can be changed in the Traveller HD Menu

Reading mode 2 (optional): This mode enhances the foreground / background contrast. Pictures and text will be displayed in the configured high contrast foreground and background colour, by default white text on a black background. The foreground and background colour can be changed or disabled in the Traveller HD Menu

Reading mode 3 (optional): This mode enhances the foreground / background contrast. Pictures and text will be displayed in the configured high contrast foreground and background colour. By default this mode is disabled. The foreground and background colour can be enabled and changed in the Traveller HD Menu

Reading mode 4 (optional): This mode enhances the foreground / background contrast. Pictures and text will be displayed in the configured high contrast foreground and background colour. By default this mode is disabled. The foreground and background colour can be enabled and changed in the Traveller HD Menu

#### Object lighting on / off

Pressing the Mode button for three seconds will turn off the object lighting. Pressing this button for three seconds again will turn the object lighting back on.

#### Snapshot

To make a snapshot, press the white Snapshot button located below the Zoom wheel. It allows you to take a temporary picture of a text or image. Pressing the Snapshot button again for 2 seconds will save the temporary image. The Traveller HD can save up to 1000 images.

#### Menu

Press the blue Menu button located at the left side of the unit, marked with the word “Menu” to activate the Traveller HD settings menu. For more information about the Traveller HD menu, please refer to chapter 4.

#### Reading line

The Traveller HD can display a reading line to help you position the Traveller straight on the document. To display the reading line, press the blue Reading Line button below the Mode button at the left side of the unit for 2 seconds. Push this button again to hide the reading line.

#### Positioning the reading line

When the reading line is activated, press the Reading Line button for 2 seconds again. The line blinks to indicate it can be moved. Press the Reading Line button to move the line to one of its three positions, top half, middle or bottom half of the screen. After 5 seconds, the reading line will stop blinking and exits modification mode automatically.

### The Traveller HD Menu

Here’s a description on the symbols you’ll find in the menu and their meaning.

Circle with an ‘I’ in the centre: Shows the battery status and firmware version

A camera symbol: Allows you to view or delete the saved snapshots

A sun: Allows you to adjust the screen brightness

A battery: Allows you to configure the power settings

A speaker: Allows you to switch the sound on and off

A light bulb: Allows you to switch the light on and off

A square with a triangle in the top right corner: Allows you to change the colours of the high contrast modes

A curved arrow pointing to the right: Allows you to reset all factory settings to default

### Activating the menu

To enter the menu, press the Menu button for 2 seconds.

### Navigating the menu

Use the Reading Line or Menu buttons to navigate between the menu items. The Mode button will activate the chosen menu item or confirm the selection. To change a selection, use the Reading Line or Menu buttons. To move back in the menu, press the Snapshot button.

### Exiting the menu

To exit the menu, press the Snapshot button or the Menu button for 2 seconds.

### Menu options

#### Menu: Information

This menu item shows the battery status and the current firmware version of the unit. In this menu, it is not possible to make any changes.

Activate the menu by pressing the Menu button for 2 seconds

Use the Menu button to move up and the Reading Line button to move down within the menu

Press the Snapshot button to go exit the menu

#### Menu: Images

This menu contains 2 submenus:

View: To view saved images

Delete: To delete saved images

#### Submenu View: To view the taken images:

Activate the menu by pressing the Menu button for 2 seconds

Use the Menu button to move up and the Reading Line button to move down within the menu. Select the menu option Images and activate this menu by pressing the Mode button

Select the View option by using the Menu and Reading Line buttons to scroll through the options. Press the Mode button to confirm your choice

Select the image you wish to view by using the Menu button to move up the list with images, and the Line button to move down the list with images. Press the Mode button to select the image

Use the Snapshot button to return to video mode

#### Submenu Delete: To delete the taken images:

Activate the menu by pressing the Menu button for 2 seconds

Use the Menu button to move up and the Reading Line button to move down within the menu. Select the menu option Images and activate this menu by pressing the Mode button

Select the Delete option by using the Menu and Reading Line buttons to scroll through the options. Press the Mode button to confirm your choice

Select the image you wish to delete by using the Menu button to move up the list with images, and the Reading Line button to move down the list with images. Press the Mode button to select the image

Press the Mode button to confirm to delete the image, or the Snapshot button to cancel

Press the Snapshot button to go back to the previous menu

#### Menu: Brightness

This menu item allows you to adjust the brightness of the display.

Activate the menu by pressing the Menu button for 2 seconds

Use the Menu button to move up and the Reading Line button to move down within the menu. Select the menu option Brightness and activate this menu by pressing the Mode button

Select the brightness level by using the Menu button to increase and the Reading Line button to decrease the brightness level. There are 5 brightness levels to choose from. The default brightness level is 5

Press the Mode button to confirm your choice

Press the Snapshot button to go back to the previous menu

#### Menu: Power

This menu item contains four submenus:

Standby: To set the time before the Traveller HD goes into standby mode

Power off: To set the time before the Traveller HD switches off

Open: To enable or disable the power-on function upon opening the Traveller HD

Close: To enable or disable the power-off function upon closing the Traveller HD

Submenu Standby: Sets the time before the Traveller HD goes into standby mode to conserve power. Pressing any button will take the unit out of standby mode. By default, the standby time is set to 15 minutes.

To adjust the standby time of the TravellerHD:

Activate the menu by pressing the Menu button for 2 seconds

Use the Menu button to move up and the Reading Line button to move down within the menu. Select the option Power and activate this menu by pressing the Mode button

Select the Standby option by using the Menu and Reading Line buttons to scroll through the options. Press the Mode button to confirm your choice

Select the time before the unit will enter Standby mode by using the Menu button to increase and the Reading Line button to decrease the time. Press the Mode button to confirm your choice. Selecting NEVER will disable the Standby function

Press the Snapshot button to go back to the previous menu

Submenu Power off: Sets the time before the Traveller HD is automatically switched off. By default, the power off time is set to 5 minutes. These 5 minutes are activated after the default standby time of 15 minutes. By default, the unit is therefore automatically switched off after 20 minutes.

To adjust the Traveller HD power off time:

Activate the menu by pressing the Menu button for 2 seconds

Use the Menu button to move up and the Reading Line button to move down within the menu. Select the menu option Power and activate this menu by pressing the Mode button

Select the Power off option by using the Menu and Reading Line buttons to scroll through the options. Press the Mode button to confirm your choice

Select the time before the unit will power off by using the Menu button to increase and the Reading Line button to decrease the time. Press the Mode button to confirm your choice. Selecting NEVER will disable the automatic power off function

Press the Snapshot button to go back to the previous menu

Submenu Open: To enable or disable the power-on function upon opening the Traveller HD:

Activate the menu by pressing the Menu button for 2 seconds.

Use the Menu button to move up and the Reading Line button to move down within the menu. Select the menu option Power and activate this menu by pressing the Mode button

Select the Open option by using the Menu and Reading Line buttons to scroll through the options. Press the Mode button to confirm your choice

To enable the power-on function upon opening the unit, select the value POWER ON by using the Menu or Reading Line button. Press the Mode button to confirm your choice. Selecting NOTHING will disable the power-on function upon opening the unit

Press the Snapshot button to go back to the previous menu

Submenu Close: To enable or disable the power-off function upon closing the Traveller HD:

Activate the menu by pressing the Menu button for 2 seconds

Use the Menu button to move up and the Reading Line button to move down within the menu. Select the menu option Power and activate this menu by pressing the Mode button

Select the Close option by using the Menu and Reading Line buttons to scroll through the options. Press the Mode button to confirm your choice

To enable the power-off function upon closing the unit, select the value POWER OFF by using the Menu or Reading Line button. Press the Mode button to confirm your choice. Selecting NOTHING will disable the power-off function upon closing the unit

Press the Snapshot button to go back to the previous menu

#### Menu: Sound

This menu item allows you to enable or disable the sounds (feedback tones). By default, the tones are enabled.

Activate the menu by pressing the Menu button for 2 seconds

Use the Menu button to move up and the Reading Line button to move down within the menu. Select the menu option Sound and activate this menu by pressing the Mode button

To enable the sounds, select the value ON by using the Menu and Reading Line buttons. Press the Mode button to confirm your choice. Selecting the value OFF will disable the sounds

Press the Snapshot button to go back to the previous menu

#### Menu: Light

This menu item allows you to enable or disable the object lighting.  By default, the object lighting is enabled.

Activate the menu by pressing the Menu button for 2 seconds

Use the Menu button to move up and the Reading Line button to move down within the menu. Select the menu option Light and activate this menu by pressing the Mode button. To enable the object lighting, select the value ON by using the Menu and Reading Line buttons. Press the Mode button to confirm your choice. Selecting the value OFF will disable the object lighting

Press the Snapshot button to go back to the previous menu

#### Menu: Colour

The Traveller HD supports four high contrast modes. For each of these four modes, the foreground and background colours can be selected. Three of the high contrast modes can be disabled if just one high contrast mode is required.

Activate the menu by pressing the Menu button for 2 seconds

Use the Menu button to move up and the Reading Line button to move down within the menu. Select the menu option Colour and activate this menu by pressing the Mode button

Select the high contrast mode by using the Menu button to move up and Reading Line button to move down in the colour submenu. Press the Mode button to confirm your choice

To select a new high contrast colour for the foreground and background, use the Menu button to move up and the Reading Line button to move down in the list of colour combinations. Select a colour combination by pressing the Mode button. High contrast modes 2, 3 and 4 can be disabled by selecting the DISABLED value

Press the Snapshot button to go back to the previous menu

#### Menu: Reset

The Traveller HD can be reset to the factory default settings. Any settings that have been adjusted will be restored to the factory defaults.

Activate the menu by pressing the Menu button for 2 seconds

Use the Menu button to move up and the Reading Line button to move down within the menu. Select the menu option Reset and activate this menu by pressing the Mode button

To restore the factory defaults, select YES by using the Menu and Reading Line buttons. Press the Mode button to confirm to reset all settings to the factory defaults. Choosing NO will leave all settings as they were

Press the snapshot button to go back to the previous menu

## Charging the battery

### Charging the Traveller HD

To charge the Traveller HD, connect the power supply to the 12V DC IN jack located on the left side of the unit. Plug the other end of the power supply into a power outlet. The LED indicator next to the 12V DC IN jack will glow orange continuously while the Traveller HD is charging. Once the unit is fully charged, the LED indicator will turn green. If the LED indicator flashes, there is a charging problem. In this case, disconnect the power supply and try again.

Charging the Traveller HD takes approximately 4 hours. A fully charged Traveller HD can operate for an average time of 3 hours, depending on the power settings. Please note that, for safety reasons, only the power supply that was delivered with the Traveller HD can be used to charge the unit’s battery.

Please note: RNIB doesn’t guarantee batteries.

### Standby and Auto Power Off

The Traveller HD will automatically go into standby mode after 15 minutes if no button is pressed or no image change is detected. Pressing any button will wake up the unit. Five minutes after the Traveller HD goes into standby mode, the unit will automatically switch off. Pressing the orange on / off button will switch it back on. The standby time and power-off time can be changed or disabled in the Traveller HD menu. Please refer to chapter 4 on how to change these settings.

### Battery warning

When the battery charge reaches below 5% of its total capacity, the unit will issue a battery warning every minute by displaying the battery-empty icon for 2 seconds. When this occurs, make sure to charge your unit as soon as possible. When the battery is empty, the unit automatically switches off.

If a unit does not switch on, please make sure it is charged.

## Appendix A: Safety and Regulatory Notices

Please read the instructions carefully before setting up your Traveller HD. Keep this user manual for future reference.

Intended Use:

The Traveller HD is designed in such a way that it can be used in a hospital environment for general purposes such as reviewing medical records. The Traveller HD cannot be used for surgical procedures in combination with life supporting systems.

Warning: Critical diagnostic decisions should not be based on images displayed by this device.

Do not expose the Traveller HD to excessive heat or direct sunlight to avoid the risk of fire

Do not remove any parts of the Traveller HD. Contact RNIB helpline if the product is faulty.

To avoid risk of electrical damage, keep your Traveller HD away from fluids and chemicals

Handle the Traveller HD with care. Rough handling will damage the internal components

Do not use the Traveller HD near inadequately shielded medical devices

Do not try to open the battery compartment or try to remove the battery

Contact your dealer to service this equipment if necessary. Do not disassemble your unit as it will void the warranty

Always unplug and switch off the unit before cleaning. Use a dry soft cloth to clean the exterior. Do not use cleaning agents or abrasive materials as they will damage your unit

Use of the Traveller HD other than described in this manual will exclude it from warranty conditions.

### Contacting Product Support

If you have questions about operating, installing or configuring your Traveller HD, please contact RNIB.

# Technical specification

Magnification: 2.4 – 30 times (+/-3%)

Viewing modes: Full colour photo mode; High contrast colour combination 1, white on black; High contrast colour combination 2, black on white; High contrast colour combination 3 (unassigned); 	High contrast colour combination 4 (unassigned)

Screen: 13,3” TFT

Battery: average 3 hours continuous use; 6 hours charging time

Integrated LED lighting

Weight: 1995 g

Dimensions: 365x240x49 mm

Operating conditions

Temperature: +10°C to 35°C / 50°F to 95°F

Humidity: < 70%, no condensation

Altitudes: up to 3000 m (9842 feet)

Pressure: 700 – 1060 hPa

Storage & transportation conditions

Temperature: +10°C to 40°C / 50°F to 104°F

Humidity: < 95%, no condensation

Altitudes: up to 12192 m (40000 feet)

Pressure: 500 – 1060 hPa

# How to contact RNIB

Phone number: 0303 123 9999

Textphone: 0845 758 5691

Web address: rnib.org.uk/shop

Postal address: RNIB, PO Box 173, Peterborough PE2 6WS, U.K.

Email: helpline@rnib.org.uk

RNIB Technology Team

Telephone 0207 391 2280

Email tfl@rnib.org.uk

## Terms and conditions of sale

This product is guaranteed from manufacturing faults for 24 months from the date of purchase.  If you have any issues with the product and you did not purchase directly from RNIB then please contact your retailer in the first instance.

For all returns and repairs contact RNIB first to get a returns authorisation number to help us deal efficiently with your product return.

You can request full terms and conditions from RNIB or view them online.

Registered Charity No. 226227

This product is CE marked and fully complies with all applicable EU legislation.

At the end of the product’s life you can return it to the supplier or manufacturer for free of charge disposal.  This is to comply with ‘The Waste Electrical and Electronic Equipment Directive’ (WEEE).

Date: December 2016

© RNIB