Ruby HD portable video magnifier

HC114

Please retain these instructions for future reference. These instructions are also available in other formats.

Contents

Special warning	2

General description	2

Orientation	3

Front	3

Back	3

Bottom edge	3

Getting started	3

Using the product	4

Battery LED descriptions	4

Inserting batteries	4

Charging NiMH batteries	5

Turning on RUBY HD	5

Button descriptions	5

Magnifying live images	6

Magnifying frozen or saved images	6

Changing colour modes	6

Switching between the last used colour mode and full colour	6

Displaying more colour modes	7

Resetting default colour modes	7

Colour modes	7

Default colour modes	7

Additional colour modes	7

Freezing an image	8

Turning LED lights off	8

Using reading line or reading masks	8

Displaying reading line	8

Displaying reading masks	9

Storage mode	9

Saving and deleting an image	9

Viewing saved images	9

Saving an image when memory is full	10

Storage mode icons	10

Transferring images to a computer using the USB cable	10

Transferring images to RUBY HD using the USB cable	11

Displaying a slide show	11

Safety and maintenance	12

Cleaning the LCD screen	12

Cleaning the RUBY HD body	12

Technical specification	12

Hints and Tips	13

How to contact RNIB	14

Terms and conditions of sale	14

# Special warning

Please note: This product is returnable within 14 days of receipt in an “as new” condition in original, undamaged packaging.

Before using Ruby® HD for the first time, you must charge the four AAA NiMH (1000 mAh) batteries. These batteries are included. A full charge takes approximately 2 hours. Refer to Battery LED Descriptions for battery status explanations. You can also use four AAA disposable alkaline batteries to operate the unit.

Do not mix NiMH batteries with alkaline batteries. Replace all batteries of the same chemistry at the same time. Do not mix new batteries with old batteries. Replace NiMH batteries with 1000 mAh NiMH batteries. Failure to follow this precaution can lead to battery failure or leakage. The risk of explosion is possible if batteries are replaced with an incorrect type. Do not use batteries that specify a MAX Charging Current below 250 mA.

Refer to Charging NiMH Batteries for battery charging procedures.

Refer to Battery LED Descriptions for battery status descriptions.

For the basics to help you get started using RUBY HD, read Quick Start.

For an overview of RUBY HD and its operation, review the information in this guide first.

# General description

The Ruby HD is a portable, handheld video magnifier that can magnify an object from 2 to 13 times its size. It has an, auto-focus HD camera that provides sharp HD quality images that are easily viewed on its full colour, 4.3-inch LCD screen. Ruby HD supports five default colour modes, and 15 additional contrasting colour modes that can easily be enabled.

The unit has a fold-away handle that allows you to hold the magnifier close to an object, press the magnification buttons for continuous zoom (2x to 13x with the handle open or 4x to 10x with the handle closed), and then freeze the image on the screen. If you like, you can then make any necessary magnification adjustments. This is ideal for viewing clothing labels, prescription labels, price tags, receipts, business cards, and more.

## Orientation

Hold the unit in front of you so that the LCD screen is facing towards you. If you’re holding it the correct way up, the two blue buttons with arrows printed on them will be on the left hand side.

### Front

On either side of the LCD display are tree buttons. The buttons to the left of the LCD display, starting at the top and moving down are:

Colour mode scroll up (blue with an arrow pointing up)

Colour mode scroll down (blue with an arrow pointing down)

Power (Green/yellow)

The buttons to the right of the LCD display, starting at the top and moving down are:

Magnification increase (yellow with a plus sign)

Magnification decrease (yellow with a minus sign)

Freeze frame (red with an image of a camera)

### Back

Turn the unit over so that the LCD display is facing down.

On the back of the unit you’ll find a handle which opens by unfolding it to the right. When the handle is open, you’ll find two LED lights with the HD camera sensor in the middle.

The handle, when open, also gives you access to the battery compartment.

### Bottom edge

On the bottom edge you’ll find a series of sockets and an LED. Starting from the left these are:

Circular power connector

Battery LED

USB port

# Getting started

Below are steps to quickly set up and use RUBY HD for the first time.

Make sure the unit is fully charged.

Turn the unit on by pressing the green/yellow button on the left hand side of the LCD display.

Then do one of the following.

Unfold the handle to hold and use the unit like a magnifying glass. This is useful when it’s necessary to magnify and read objects such as labels or details on cans, packages, pill bottles, and more

With the handle folded closed, place the unit on a flat document such as a newspaper or magazine, a bill or receipt, a letter, and so on

Adjust the magnification using the yellow buttons on the right hand side of the display.

Select a colour mode using the colour mode buttons on the left hand side (printed with and up and down arrow), to find the contrasting colours that best suit your vision needs.

To freeze the image on the LCD screen so that you may take your time reading details in the image, press the red freeze frame button on the right hand side of the display.

To save the image or return to live view, press the freeze frame button again.

# Using the product

Once you become comfortable using RUBY HD, try the following advanced features.

Turn the LED reading lights on or off to adjust for glare and reflections when viewing photographs or glossy magazine pages.

Use the reading line or reading masks to help you maintain your place while reading text.

Save, view, and delete images stored on the unit.

For additional storage, transfer images from the unit to your computer.

## Battery LED descriptions

Green – Solid: Battery charged – power adapter connected

Green – Flashing: Battery charging – power adapter connected

Red – Flashing: Battery low

Red – Solid: Error – unplug power adapter, wait a few seconds, and plug in again. If this condition persists, change the batteries

No LED: Battery charge ok, power adapter not connected; or RUBY is off

## Inserting batteries

Fully open the handle, and remove the battery cover by sliding it in the direction of the imprinted arrow (to the right).

Within the handle are two separate battery compartments, one at the top and one at the bottom. The batteries sit within these two compartments horizontally.

Insert the batteries in the following positions:

Top compartment: positive pointing to the left on both batteries

Bottom compartment: positive pointing to the right on both batteries

Replace the battery cover by sliding it back on from right to left, and close the handle.

Make sure that batteries are inserted using the correct polarity.

## Charging NiMH batteries

Plug one end of the power adapter into the unit and the other end into a wall outlet.

The battery indicator LED on the bottom blinks green to show that the batteries are charging. For more, see Battery LED Descriptions.

The LED stops blinking and glows a steady green once the batteries are charged.

Unplug the power adapter from the unit. The battery indicator LED turns off.

You can now use your RUBY HD for approximately two hours of continuous use.

When the batteries are low, the battery indicator LED flashes red. Connect the power adapter and plug it in to recharge the NiMH batteries.

Note: If you decide to replace the supplied NiMH batteries, replace all four at the same time with 1000 mAh NiMH batteries with a MAX Charging Current above 250 mA.

## Turning on RUBY HD

Press the green/yellow button to turn on the unit. After a few seconds, the battery status icon displays on the screen.

Press the button again to turn off the unit.

Note: If it is left on and no buttons are pressed, it automatically turns off after 30 minutes to avoid draining the batteries.

## Button descriptions

Power (Green/Yellow): Press to turn power on. Press it again to turn power off.

Magnification (Yellow): Press and HOLD for continuous zoom magnification with live images. When viewing frozen images, press and release to incrementally increase or decrease magnification.

Colour Mode (Blue): Press to cycle through five default colour modes and 15 additional colour modes. For a complete list, refer to Colour Modes section.

Freeze Frame (Red): Press to freeze the current image. Press it again to turn off

Freeze Frame mode and return to live view.

## Magnifying live images

When viewing a live image, you can use continuous zoom magnification between 2x to 13x with the handle open, or 4x to 10x with the handle closed.

Press and HOLD the yellow PLUS button to zoom in

Press and HOLD the yellow MINUS button to zoom out

### Magnifying frozen or saved images

You can freeze and then save an image that displays on the LCD screen. When viewing a frozen or saved image, you can zoom in or out in incremental steps by pressing the yellow buttons.

For steps to freeze an image, refer to Freezing an image.

To access saved images, refer to Saving and Deleting an Image.

## Changing colour modes

A colour mode is a pre-defined colour combination (for example, yellow text on a blue background) that you can select when reading items with RUBY HD.

The unit has five default colour modes: Full Colour; Black on White (high-contrast positive); White on Black (high-contrast negative); Yellow on Blue; Yellow on Black; and 15 additional colour modes. For a complete list, refer to Colour Modes.

Press the blue arrow buttons to change the current colour Combination on the LCD screen.

The blue UP arrow button cycles in one direction through the colour combination list while the blue DOWN arrow button cycles in the other direction.

### Switching between the last used colour mode and full colour

RUBY HD provides the convenience of quickly switching between the last colour mode used and full colour, or vice versa.

This shortcut is useful when looking at a live image (for example, while holding and reading a document) and using a colour mode that provides the best contrast for you. If you need to move the unit to a different part of the document, it may be easier to switch to full colour, move to the new location and then return to your colour mode selection and continue reading.

To do this:

Press and HOLD the green/yellow button, and then press the blue DOWN arrow button. The screen changes from one mode to the other

To switch back, repeat the same button sequence again

## Displaying more colour modes

RUBY HD has five default colour modes. You can also activate and choose from a variety of 15 other colour modes. Once a colour mode is available, you can easily switch to it using the blue arrow buttons.

To add or remove other colour modes:

Press and HOLD the green/yellow button and then press the blue UP arrow button to enter Colour Selection mode. The Enable check box displays indicating that the current colour mode is active

To disable the current colour mode, press the blue DOWN arrow while STILL holding the green/yellow button. This button sequence clears the check box

To scroll to the next colour mode, press the blue UP arrow while STILL holding the green/yellow button. If the check box is selected, the colour mode is enabled. If the check box is cleared, the colour mode is disabled

To enable or disable a colour mode, press the blue DOWN arrow while STILL holding the green/yellow button to select or clear its check box

Repeat steps 3 and 4 to continue adding or removing colour modes

When you are finished loading colour modes, release all buttons. Any colour mode changes made will be saved, and the unit will return to normal operating mode

### Resetting default colour modes

If you have added or removed colour modes that display on the screen, you can always restore RUBY HD to its five default colour modes.

Press and HOLD the green/yellow button and the blue UP arrow button simultaneously for 15 seconds.

## Colour modes

There are five factory default colour modes and 15 additional colour modes that you can make active.

### Default colour modes

Full Colour (always available, cannot be disabled)

Black on White – high-contrast positive

White on Black – high-contrast negative

Yellow on Blue

Yellow on Black

### Additional colour modes

Black on Yellow

Blue on Black

Black on Amber

Green on Black

Blue on Yellow

Violet on Black

Black on Green

Red on Black

Black on Violet

White on Blue

Black on Red

Red on White

Black on Blue

Amber on Black

Black on Light Blue

## Freezing an image

Freezing an image on the LCD screen can be useful for reading labels on items on a store shelf. By holding the unit close to the item and freezing the image, you can then hold it close enough for you to read.

Press the red button to freeze the image. If you like, press the yellow PLUS button to increase magnification, or the yellow MINUS button to decrease magnification.

Press the red button again to turn off Freeze Frame mode and return to the live view.

Note: To save a frozen image, press and HOLD the red button for three seconds. Refer to Saving and Deleting an Image for more information.

## Turning LED lights off

When you turn on RUBY HD, the LED lights also turn on. To avoid glare when viewing reflective surfaces, you can turn off the LED lights.

Press and HOLD the green/yellow button, and then press the red button. The LED lights turn off.

To turn the lights on again, press and HOLD the green/yellow button, and then press the red button.

## Using reading line or reading masks

The reading line is a horizontal line that displays on the screen. Reading masks block part of the screen to show a horizontal slice of the screen. Use these items to help you locate and maintain your place while viewing an image. When using the button sequence as described below, the unit cycles through displaying the reading line, the reading masks, and then no reading line or masks.

### Displaying reading line

Press and HOLD the green/yellow button and then press both yellow buttons. The reading line displays on the screen as shown in the next figure.

Press and HOLD the green/yellow button and then press the yellow PLUS button or the yellow MINUS button to move the reading line up or down on the screen.

### Displaying reading masks

Press and HOLD the green/yellow button and then press both yellow buttons again to remove the reading line and display the reading masks on the screen as shown in the next figure.

Press and HOLD the green/yellow button and then press the yellow PLUS button or the yellow MINUS button to increase or decrease the distance between the masks.

To remove reading masks from the screen, press and HOLD the green/yellow button and then press and HOLD both yellow buttons.

## Storage mode

Storage mode can save approximately 80 images. When you first store an image, it is saved with the current magnification and colour settings just as displayed on the screen. When viewing a saved image, you can change the magnification level.

### Saving and deleting an image

After freezing an image on the screen, you can save it by doing the following.

Press and HOLD the red button for three seconds to enter Storage mode.

The Save Image check box is automatically selected and displays for three seconds. This indicates that the image will be saved after exiting Storage mode and returning to live view.

To delete an image while in Storage mode:

Press and HOLD both yellow buttons to clear the check box. When you exit Storage mode, the image is deleted

Press and HOLD the red button for three seconds to exit and return to live view

### Viewing saved images

RUBY HD can store approximately 80 images. You can easily scroll through the images using the blue arrow buttons.

Press and HOLD the red button for approximately six seconds to enter Review mode.

To scroll forward through the saved images, press the blue UP arrow.

To scroll backward through the saved images, press the blue DOWN arrow.

Press and HOLD the red button for approximately three seconds to exit and return to live view.

### Saving an image when memory is full

RUBY HD can store approximately 80 images. If you try to save another image when the unit’s memory is full, the Memory Full icon displays on the screen.

To add another image, you must first remove one or more saved images from memory.

Press the blue UP arrow or the blue DOWN arrow to step to an image that you want to delete.

Press both yellow buttons to clear the check box.

Press and HOLD the red button for three seconds to exit Storage mode. The new image is saved, and all unchecked images are deleted.

Note: To free space on the unit, you can also move images to a computer. For more information, refer to Transferring Images to a Computer Using the USB Cable.

### Storage mode icons

Save: Press the two yellow buttons at the same time to select the check box. The image is saved when you exit Storage mode.

Delete: Press the two yellow buttons at the same time to clear the check box.

The image is deleted when you exit Storage mode.

Memory Full: Indicates that memory is full and no more images can be saved on the unit. You must mark one or more images for deletion before you can save the current image.

### Transferring images to a computer using the USB cable

Images stored on RUBY HD can be transferred to your computer using the supplied USB cable. To do this, connect the supplied USB cable to the unit and the computer.

When connected:

The USB symbol and battery icon briefly display on the LCD screen

The battery icon indicates the current battery status. Images do not display on the screen while the unit is connected to a computer’s USB port.

Note: A USB port does not provide enough power to charge the NiMH batteries. Use the power adapter to recharge low batteries.

RUBY HD displays as an external device in Windows Explorer or Finder (Mac)

Open RUBY HD’s DCIM folder and use the drag and drop method to move or copy one or more images to a folder or the desktop on your computer. Images are named and are numbered in the order saved, for example, IMG_0001.bmp, IMG_0002.bmp, and so on as shown in the next figure.

When you are finished transferring files, make sure that you safely eject (remove) the unit from your computer.

Note: To safely disconnect the unit and protect your data, always follow your operating system’s procedures for removing a USB device.

### Transferring images to RUBY HD using the USB cable

Any image moved from RUBY HD to your computer can easily be moved back to the unit.

Note: Only images saved by RUBY HD can be copied back to the unit.

Make sure the unit is connected to your computer using the supplied USB cable

Locate the image on your computer using Windows Explorer or Finder (Mac)

Select the image and drag it to RUBY HD’s DCIM folder

When you are finished transferring files, make sure that you safely eject (remove) the unit from your computer

Note: To safely disconnect the unit and protect your data, always follow your operating system’s procedures for removing a USB device.

### Displaying a slide show

You can create a slide show that loops continuously using the images saved on the unit. Each image displays for approximately five seconds. The order that images display is based on their file names, for example, IMG_0001.bmp, IMG_0002.bmp, and so on.

To rearrange the order that images display, you can transfer them to your computer, rename the files in the order that you like, and then transfer them back to the unit. (The file names should not be longer than eight characters followed by the BMP file extension.) To move files between the unit and computer, refer to the transfer procedures.

Note that when in Slide Show mode, the 30-minute power-off timer is disabled.

To start the slide show, do the following:

Press and HOLD the red button for approximately six seconds to enter Review mode

Press and HOLD the green/yellow button, and then press the blue UP arrow.

The first image stored on the unit, based on its file name, displays on the LCD screen for approximately five seconds followed by the second image, the third, and so on

Press and HOLD the red button for approximately three seconds to exit Slide Show mode and return to live view

## Safety and maintenance

Do not attempt to repair the unit or open its case. This product contains no user serviceable parts. Any unauthorized attempt to service or replace internal components will void the product warranty

Keep the unit away from wet areas, rain, and other sources of liquids. Do not submerge the unit

Always operate the unit in a place where the temperature is between 10° and 35° C (50° and 95° F)

Do not store in places subject to temperature extremes such as a parked car

Do not force any connector into the unit’s power port. The power connector fits easily into the port

### Cleaning the LCD screen

Turn off and unplug the unit before cleaning the LCD screen

Always use a clean microfiber cloth

Very gently wipe the cloth across the screen. Do not press hard on the cloth or screen

If you use a cleaning liquid, use an appropriate LCD cleaning liquid. You can also use distilled water, isopropyl alcohol, or vinegar mixed with water at a concentration of no more than 10 per cent vinegar. Note that tap or mineral water may cause spotting on the screen. Do not leave any liquid on the screen. Repeat this procedure for hard to remove smudges

Do not spray any cleaning solutions directly on the LCD screen

Do not use a cleanser that contains acetone, ethyl alcohol, ethyl acid, ammonia, or methyl chloride

Do not use a paper towel to clean the LCD screen

### Cleaning the RUBY HD body

Make sure the unit is unplugged. Use a lightly dampened, soft, clean cloth with water or mild detergent. Do not use alcohol, solvents, abrasives, or aerosol sprays

# Technical specification

LCD widescreen: 4.3 inches (109 mm)

Body size: 4.9 inches high (125 mm) 2.9 inches wide (74 mm) 1.4 inches deep (36 mm)

Weight: 8.0 oz. (227 grams)

Colour modes: Five factory default colour modes (Full Colour; Black on White (high-contrast positive); White on Black (high-contrast negative); Yellow on Blue; Yellow on Black), and 15 additional colour modes

Magnification range: 4x to 10x zoom (handle closed) 2x to 13x zoom (handle open)

Maximum saved images: Approximately 80 bitmap (BMP) images

Camera: HD auto-focus camera module

Image resolution: 800 x 450 pixels

Colour: 24-bit

Battery: Four AAA NiMH rechargeable (1000 mAh) batteries; approximately 2 hours of continuous use; charges in approximately 2 hours, or Four AAA disposable alkaline batteries

Note: Only use the supplied power adapter to charge the unit’s battery. Do not use batteries that specify a MAX Charging Current below 250 mA.

# Hints and Tips

The unit does not turn on.

Press the green/yellow Power button. If the unit does not turn on, charge the batteries

Make sure the batteries are inserted correctly. Note: A USB port does not provide enough power to charge the NiMH batteries. Use the power adapter to recharge low batteries

The screen is blank.

When the unit is connected to a computer via USB, the screen is blank

Turn on the LED lights

Turn the unit off and then on again

Verify that the item you want to magnify is positioned correctly under the camera window

Press the yellow Magnification buttons to step through the magnification levels

Press the blue Colour Mode buttons to step through the colour modes

The battery indicator LED is flashing red.

Charge the NiMH batteries, or replace the AAA alkaline batteries. (Do not mix battery chemistries)

If you replace the rechargeable batteries, be sure to use 1000 mAh NiMH batteries

The battery LED is solid red while the power adapter is connected to the unit.

A battery error has occurred. Unplug the power adapter from the unit and plug it in again

Charge the NiMH batteries for at least 2 hours, or replace with AAA alkaline batteries. Do not charge alkaline batteries

If the problem continues, disconnect the power adapter and call RNIB Helpline.

The battery indicator LED does not flash green, even though the power adapter is connected and plugged into a wall socket.

Ensure that the small end of the power adapter is firmly plugged into the unit’s power port

Ensure that the outlet has power and is not malfunctioning. If the outlet is connected to a wall switch, make sure the switch is on

The NiMH batteries are not charging.

Make sure the batteries are inserted correctly. (Do not replace batteries while the power adapter is connected)

Use the supplied power adapter to charge the unit. Note that a USB port does not provide enough power to charge the batteries

Make sure the small end of the power adapter is firmly plugged into the unit’s power port

Ensure that the outlet has power and is not malfunctioning. If the outlet is connected to a wall switch, make sure the switch is on

Some batteries have low charge rates and specify a “MAX Charging Current.” DO NOT USE batteries that specify their MAX Charging Current as being below 250 mA

There are smudges or blemishes on the screen.

Clean the LCD screen as described in Cleaning Procedures

Text is too small or too large to read.

Press the yellow Magnification buttons to increase or decrease magnification. For live images, press and HOLD a magnification button for continuous zoom magnification. For frozen or saved images, press a magnification button to zoom in or out one step at a time

LED lights produce glare against a reflective surface.

Press and HOLD the green/yellow Power button, and then press the red Freeze Frame button to turn off the LED lights

The unit turns off after reading for 30 minutes.

This is expected behaviour. The unit turns off after 30 minutes if no buttons are pressed. This extends battery life.

# How to contact RNIB

Phone number: 0303 123 9999

Textphone: 0845 758 5691

Web address: rnib.org.uk/shop

Postal address: RNIB, PO Box 173, Peterborough PE2 6WS, U.K.

Email: helpline@rnib.org.uk

RNIB Technology Team

Telephone 0207 391 2280

Email tfl@rnib.org.uk

Email for international customers exports@rnib.org.uk

## Terms and conditions of sale

This product is guaranteed from manufacturing faults for 24 months from the date of purchase.  If you have any issues with the product and you did not purchase directly from RNIB then please contact your retailer in the first instance.

For all returns and repairs contact RNIB first to get a returns authorisation number to help us deal efficiently with your product return.

You can request full terms and conditions from RNIB or view them online.

Registered Charity No. 226227

This product is CE marked and fully complies with all applicable EU legislation.

At the end of the product’s life you can return it to the supplier or manufacturer for free of charge disposal.  This is to comply with ‘The Waste Electrical and Electronic Equipment Directive’ (WEEE).

Date: January 2017

© RNIB