# Ideal hand magnifier

2x/4D - 4x/12D

MAG01, MAG02, MAG04, MAG05

Please retain these instructions for future reference. These instructions are also available in other formats.

# Importance of a low vision assessment

RNIB and Action for Blind People strongly advise anyone with visual impairment to have a low vision assessment. This is an NHS funded service usually accessed at your local hospital eye clinic or run by a local organisation. Referral to the clinic is usually by your General Practitioner (Doctor), Optometrist or Ophthalmologist. The assessment is free of charge and available to anyone with low vision. You do not have to be registered as sight impaired to access this service.

Low vision means that you will be finding it hard to see things as clearly as you would like to, even after you have had your eyes tested and are wearing the correct spectacles or contact lenses.

At the assessment a qualified low vision practitioner will check your vision and assess your suitability for low vision aids such as magnifiers. These clinics are usually able to provide at least one magnifier to you, free of charge. As magnifiers can be difficult to use initially, the practitioner will help you to get the best out of the equipment they prescribe. If you have been discharged by your eye specialist, you can ask your GP or Optometrist to refer you to the nearest clinic.

# Choosing a magnifier

RNIB's booklet 'Choosing your magnifier' is designed to help people with a visual impairment understand the various types of magnifier that can be used for specific tasks. This booklet is available from RNIB's Helpline in large print, audio or braille, or can be downloaded from rnib.org.uk

# Warning! Important information

Do not leave your magnifier in direct sunlight when it is not being used. The intensifying effect of the lens could become a fire hazard in direct sunlight. Use your protective cover (if provided) and always store in a safe place.

Never look at the sun directly through a magnifying lens as it could damage your eyes.

Do not look directly at the light source in illuminated magnifiers as LEDs are very bright.

Avoid impacting, banging or dropping your magnifier, as well as moisture and high temperatures which may cause damage.

Avoid putting your hands or fingers on the lens of your magnifier - always use the frame or handle.

# General description

These economically priced magnifiers have convex lenses, lightweight handles and transparent frames, and are ideal to use in the kitchen or at the side of the bed for spot reading. They are suitable for short term, as opposed to long term use and are available between 2x and 4x magnification.

Please note: The option to have either a round or rectangular lens is in 2x/4D only. All other magnifiers have round lenses.

MAG01: 2x/4D, rectangular lens 10cm x 5cm

MAG02: 2x/4D, lens diameter 10cm (round)

MAG04: 3x/8D, lens diameter 6cm (round)

MAG05: 4x/12D, lens diameter 5cm (round)

## Orientation

Holding the magnifier in front of you, the lens is contained within a clear plastic surround which goes on to form the handle.

# Using the product

When using a hand held magnifier you will need to hold it in the correct position and distance off the page, to focus. You can do this by placing the magnifier flat on the page and slowly bring it up towards your eye until it is in focus. If you can bring the magnifier (and print together) nearer your eye you will be able to see more words in one view. If the image appears upside down, the magnifier and print are too far away from your eye and you will need to bring the magnifier and page nearer to your eye (maintaining the focal position).

Another way of using your hand held magnifier is to hold the magnifier up to your viewing eye (looking through the centre of the lens), and bring up the reading material until it becomes in focus and is clearer to see.

# Hints and Tips

## Aftercare

Proper care of your magnifier means it will provide you with many years of untroubled reading. Clean the lens with a damp cloth (ideally a damp micro-fibre cloth). Never use solvents such as alcohol, benzene or other cleaning agents as these can damage the lens.

You may find small lines that look like hairline cracks at the edge of lightweight lenses or in the plastic frame. These are flow lines that occur during the production process, but they do not affect the function or durability in any way.

It is essential that the reading material is placed on a firm and flat service. If you are not using your table, you can also achieve this by using a clipboard (available from RNIB - product code DW38). A cushion or tray may also be useful.

Magnifiers usually work best with the spectacles that you have been prescribed by your low vision professional. If you find it difficult to keep your place when reading, try using your finger to mark the start of each line. Holding a magnifier close to your eye and then bringing what you want to see up to it will often help you see more letters and words at a time. Try moving the book or page from side to side rather than moving the magnifier or your eyes. If you find your eyes are getting tired, take a break and start again when you feel better.

## Effective lighting

RNIB and Thomas Pocklington's booklet 'Make the most of your sight, improve the lighting in your home' demonstrates good practice by giving ideas, hints and tips. It explains how to light your home more effectively, as well as explaining different types of lighting and their benefits. It is available in large print, audio and braille from RNIB's Helpline or you can download it from our website.

# How to contact RNIB

Phone number: 0303 123 9999

Textphone: 0845 758 5691

Postal address: RNIB, PO Box 173, Peterborough PE2 6WS, U.K.

Email: shop@rnib.org.uk

Web address: www.rnib.org.uk

Email for international customers: exports@rnib.org.uk

## Terms and conditions of sale

This product is guaranteed from manufacturing faults for 12 months from the date of purchase.  If you have any issues with the product and you did not purchase directly from RNIB then please contact your retailer in the first instance.

For all returns and repairs contact RNIB first to get a returns authorisation number to help us deal efficiently with your product return.

You can request full terms and conditions from RNIB or view them online.

Registered Charity No. 226227

Date: February 2014

© RNIB