Yoyo foldable pocket magnifier 3x

MAG106

Please retain these instructions for future reference. These instructions are also available in other formats.

# Special warning

- Never look directly at the LEDs.

- Do not leave the lens in direct sunlight as it could cause a fire hazard.

# General description

This compact foldable pocket LED magnifier is ideal to carry in your pocket. It has 3 bright LEDs that produce 380 lux at 15cm; the acrylic 5.5cm (2.17") lens provides 8 dioptres of magnification (3.0x). The Yoyo light includes a wrist strap for your convenience to use as needed.

Requires 3 x AAA batteries (not included).

## Orientation

Position the unit in front of you so that there is a rounded semi-circle shaped recess closest to you on the top of the unit. You can insert your finger here to lift the lid that protects the magnifier lens.

### Back

At the back of the unit centrally in the top edge of the lower casing are 2 small holes where the wrist strap connects.

### Base

On the underside is the battery compartment.

### Internal

When you raise the top section away from the lower section, the button for the LEDs is revealed. This is positioned towards the front on the top face of the lower section. It is slightly dipped and is contrasted in red against the white background.

# Using the product

To use raise the top section of the unit away from the base ensuring that you hold the base for stability. Once raised you can adjust its position forwards and backwards or up and down. Press the button to turn on the LEDs for illumination.

## Battery replacement

To change batteries turn the unit over. On the base towards the side where the on/off button is, there is a recess next to a series of ridges; this is the lever point for the cover. Push the lever piece towards the rest of the battery cover, using a flat head screwdriver. The cover will lever up and off. Inside there is a compartment for 3 AAA batteries. Place the flat end of the batteries against the springs.

Once inserted, replace the cover by placing the cover back on top - place the end of the cover with 2 tabs into the inner edge first. Then lever down. It will click back into place.

# How to contact RNIB

Phone number: 0303 123 9999

Textphone: 0845 758 5691

Web address: rnib.org.uk/shop

Postal address: RNIB, PO Box 173, Peterborough PE2 6WS, U.K.

Email: helpline@rnib.org.uk

Email for international customers exports@rnib.org.uk

## Terms and conditions of sale

This product is guaranteed from manufacturing faults for 24 months from the date of purchase.  If you have any issues with the product and you did not purchase directly from RNIB then please contact your retailer in the first instance.

For all returns and repairs contact RNIB first to get a returns authorisation number to help us deal efficiently with your product return. You can request full terms and conditions from RNIB or view them online.

Registered Charity No. 226227

This product is CE marked and fully complies with all applicable EU legislation.

At the end of the product’s life you can return it to the supplier or manufacturer for free of charge disposal.  This is to comply with ‘The Waste Electrical and Electronic Equipment Directive’ (WEEE).

Date: June 2017

© RNIB