AmbuTech aluminium guide cane

MG16, MG18, MG20, MG22, MG24, MG26, MG28, MG29 MG30, MG31, MG32, MG33, MG34, MG35

Please retain these instructions for future reference. These instructions are also available in other formats.

# General description

The following canes are covered within these instructions:

MG16 (pencil tip) MG29 (roller tip) – 85cm

MG18 (pencil tip) MG30 (roller tip) – 90cm

MG20 (pencil tip) MG31 (roller tip) – 95cm

MG22 (pencil tip) MG32 (roller tip) – 100cm

MG24 (pencil tip) MG33 (roller tip) – 105cm

MG26 (pencil tip) MG34 (roller tip) – 110cm

MG28 (pencil tip) MG35 (roller tip) – 115cm

AmbuTech guide canes are made from aluminium and are available fitted with either a hook pencil or roller tip. They are available in seven lengths from 85cm to 115cm.

A guide cane should always point to the floor and can be used in a diagonal position across the lower part of the body for protection, or to scan for kerbs and steps. The top of the cane should reach just above waist level when standing upright and the tip of the cane touching the ground.

Guide canes are not to be used for supporting a person's body weight and should initially be purchased with the advice of a professional, such as a mobility officer or physiotherapist. A guide cane can help with the transition from using a symbol cane to long cane training.

## Changing the tip

### Canes fitted with a Cordlock™

The Cordlock™ is a white plastic clip, which stops the elastic slipping down the cane shaft when changing the tip. From 2013, most Ambutech canes are now fitted with a Cordlock™.

- Pull the tip out of the end section of the cane until a knot in the cord and a small piece of plastic, which is the Cordlock™, appears.

- Allow the Cordlock™ to settle across the end of the cane

- Unhook the old tip and hook on the replacement tip keeping the tip and elastic under tension

- Fold the Cordlock™ so it sits parallel to the elastic and faces away from the knot

- Let the elastic slide back into the cane shaft under tension and with the hook through the elastic

### Replacing hook tips on older canes

- Pull the tip out of the end section of the cane until a knot in the elastic appears

- Slip a pen or similar object into the gap between the knot and the cane

- Release the elastic carefully until the pen rests across the end of the cane

- Unhook the old tip and hook on the replacement tip

- Remove the pen and allow the tip to sit back into the end section of the cane under tension, and with the hook through the elastic

## Accessories

- Replacement tips - hook style pencil tip (MP27) or roller tip (MP26)

- AmbuTech belt-pack cane holder - a black multi-purpose storage belt with one large and one small pocket and a holster for your cane (MP109)

- Ambutech cane renewal kit – contains everything you need to keep your aluminium  guide cane looking like new (MP106)

# Hints and Tips

## Looking after your cane

It is recommended to clean the joints regularly with a damp cloth.

Do not use the cane if there is evidence of the elastic cord fraying.

Check for excessive wear of the cane tip and replace when necessary.

# How to contact RNIB

Phone number: 0303 123 9999

Textphone: 0845 758 5691

Postal address: RNIB, PO Box 173, Peterborough PE2 6WS, U.K.

Email: shop@rnib.org.uk

Web address: www.rnib.org.uk

Email for international customers: exports@rnib.org.uk

## Terms and conditions of sale

This product is guaranteed from manufacturing faults for 12 months from the date of purchase.  If you have any issues with the product and you did not purchase directly from RNIB then please contact your retailer in the first instance.

For all returns and repairs contact RNIB first to get a returns authorisation number to help us deal efficiently with your product return.

You can request full terms and conditions from RNIB or view them online.

Registered Charity No. 226227

Date: February 2014

© RNIB